## Slide 1: Proof of Concept Virtual World Workflow
Matlab to generate Noisy texture (filt2d is mxn convolution of 1s)
  R = rand(1024)*255;
  G = filt2d(rand(1024),'avg',50,50);G = G - min(G(:));G = G * 255/max(G(:));
  B = filt2d(rand(1024),'avg',150,150);B = B - min(B(:));B = B * 255/max(B(:));
  RGB(:,:,1)= R;RGB(:,:,2)= G;RGB(:,:,3)= B;
  imwrite(uint8(RGB),'test.png');
Blender to manually generate scene
  101 640x480 pixel images along a path at 15m elevation (exact X,Y,Z positions unknown)
  13 GCPs, nine at Z = 0.125m, four at Z = 5m
  Ground plane at 0
  Random basic shapes, random sizes, shading “on” from 4 light sources
CloudCompare to do a points to mesh difference
  Used Dense Photoscan Output using all GCPs

## Slide 2: Blender
25m x 25m
Pyramids
Cones
Cylinders
Rectangular prisms
Spheres
Donuts
etc
FLIGHT PATH

## Slide 3: Photoscan
Black Hole in middle was due to a rendering issue in the imagery, but photoscan actually tried to make points to put there even when there was no texture at all.

## Slide 4: CloudCompare
Caxis = [-0.05 0.05]
Photoscan
25m x 25m
ERRORS!

## Slide 5: Photoscan
3 meters flat water
Shadows due to output rending from blender. No texture in raw imagery.
Some structures half in water
Colored blue just for this figure

## Slide 6: CloudCompare
3 meters flat water
Refraction 1.33
*fixed focal length with truth
caxis = [-0.4 0.4]
BIG ERRORS!

## Slide 7: With 3 meters water vs with no water
caxis = [-0.4 0.4]
caxis = [-0.05 0.05]

## Slide 8
caxis = [-0.2 0.2]
No Water
Intrinsic Float
Water
Intrinsic Fixed
Water
Intrinsic Float

## Slide 9: Extra: Photoscan Results
700
700
0
0
0
0
0
320
240
0
0
0
0
Actual Values
Intrinsics
GCPs
(all GCPS used in adjustment)
~49 degree FOV Nadir at 15m altitude
5 meters between horizontal lines
Flew Cross hatch pattern (N-S, and E-W)

## Slide 10: Problem with other way we talked about
If the cameras have accurate poses, we’ll get great agreement on where the point should be in pixel space
But the resultant pointcloud won’t have a high accuracy here!

## Slide 11: Problem with other way we talked about
And since we already know camera poses from Blender, we can just calculate the camera pose errors directly
To better quantify accuracy, we should look at the matches the software used
  *I have mixed feelings about diving into the photoscan matching output, on one hand I want this methodology to be software agnostic, but on the other hand I want to know what photoscan is doing. We could probably utilize this, or a similar, methodology on any other software that outputs camera poses though
error
error
calculated
truth
calculated
truth

## Slide 12: Exported matches from Photoscan
dat file
filename
Keypoint id x pixel ypixel
Matlab to decode matches

## Slide 13: Visual validation of my Matlab code Photoscan(left) Matlab(right)

## Slide 14: Relative Accuracy
High Accuracy
Least Squares to find point of intersection and standard deviation of XYZ points
Low Accuracy

## Slide 15: Do this to all the points using the matches in Matlab
Now for each coordinate export:
  Std(X)
  Std(Y)
  Std(Z)
  Or some type of covariance
Then Validate this predicted error with actual

## Slide 16: Relative/Absolute Accuracy
Previously described method gives “relative” accuracy
To quantify absolute, we need:
  How well is an image mapped to a GCP?
  How well have images been mapped as we get away from GCPs?
  Need to quantify an uncertainty metric for how well two images are mapped to each other
    How many points in each image are matched?
    How well are points in each image matched to each other?
    Are other images matching too?
  Uncertainty between images should be an uncertainty in rotation and translation
  We can then propagate those errors to farther away images
  Once we have an uncertainty for our camera orientation, we can propagate that error through in combination with the relative accuracy to get a total error estimate

## Slide 17: Absolute Accuracy
Degrades farther from GCPs, and quickly if poor matching between images
A
B
C
D
E
F
G
H

## Slide 18: SFM Sensitivity from VDOS Flights
Higher Altitude degraded much quicker than lower altitude, despite being fewer images away.
So my hypothesis was that the accuracy of matches between images was worse than that at lower altitudes. (flip between slides to see)

## Slide 19: Once Absolute Accuracy Calculated
Can we now perform a weighted least squares for relative depth?
Point at magenta star is seen in D and E
Should we weight D more heavily?
A
B
C
D
E

## Slide 20: Relative Accuracy Weighting based on orientation accuracy
Weighted higher for green image keypoint matches
Is this iterative? Or redundant?
  Because absolute accuracy is calculated based on this first least squares matching
Could also develop a confidence for where the keypoint is in the image, and weight points near edge of images(higher distortion) lower

## Slide 21: todo
Lit Review
  How to make robust, noisy texture for keypoint matching?
  How to calculate relative and absolute accuracy of pointcloud?
  How to calculate cloud to mesh distance calculations?
  What traditional cameras and flight patterns used in SFM accuracy tests?
    Overlap, sidelap, focal length, etc
  How have others quantified error in SFM pointclouds?
  Other pointcloud calibration test scenes (What shapes do other people use?)
Better Understand Blender
  Python scripting
  Texture mapping
  Accurate, (explicit) camera placement (not just follow path)
  Test Blender agorithms to make sure accurate images being made

## Slide 22: Todo (cont)
Layout all the potential experiments
  There’s a ton
  Select a good first experiment
Layout first test scene to achieve first experiment
  Layout on paper different shapes, sizes, textures, etc