## Slide 1: Virtual SFM

## Slide 2: What is SFM-MVS
Generating 3d georeferenced pointcloud from imagery
SFM to calculate poses
MVS to generate dense pointcloud

## Slide 3: Where is current research focused
Accuracy
Applications

## Slide 4: Limitations in current research
Time ($) to acquire imagery, collect control data with GPS/Lidar
Lack of control of independent variables
  Object texture, sunlight, camera positioning, camera intrinsics, camera exposure, camera blurring
Lack of accuracy of control data
  GPS and lidar have errors which propagate through into the assessment
Lack of repeatability
  Difficult for two researchers to do the same exact experiment

## Slide 5: Concept: Virtual World for Experiment Design
You can simulate cameras, imagery, texture, lighting, refraction, etc, in a controlled environment with known accuracies
Exact placement of objects and cameras

## Slide 6: Big Picture
User generates XML Files to generate data
  Scene
  Sensor
  Trajectory
Render Engine Generates Imagery, control data
User runs SFM-MVS software how they’d like
Accuracy Metric Calculations
  Point to plane, density, slope, aspect, noise, etc
User tests hypothesis using accuracy metrics

## Slide 7: Part I: Imagery+Metadata Generation
Scene.xml, Sensor.xml
Trajectory.xml
SceneLibrary.xml
Renderer
Control.txt
Log.txt
Marker.txt
Model.obj
Sensor.xml
Trajectory.txt
SFM-MVS
Software
Pointcloud.las
CameraPoses.txt
CameraIntrinsics.txt
Software to allow geomatics/SFM researchers an easy method to generate simulated UAV imagery
Ideally someone would get the “output” folder and have no idea that it was from a virtual environment and not a real UAV
images.JPG
Image
Filtering
(distortion, noise, etc)

## Slide 8: Part II: Accuracy Assessment
Give users of part I an easy way to assess a bunch of metrics from their pointcloud
Make it easier to test hypotheses by making the analysis easier
Pointcloud.las
CameraPoses.txt
CameraIntrinsics.txt
Accuracy Assessment
Accuracy
Density
Slope
Curvature
Pose error
Calibration error
etc

## Slide 9: Part III: Leverage Workflow for experiments
Effect of Nadir vs Oblique Imagery on pointcloud accuracy and density
Effect of RTK GPS on accuracy in different environments
Effect of texture on pointcloud accuracy
Effect of sidelap on accuracy
etc

## Slide 10: Using Blender + Python Scripting as Renderer
Developed workflow to make and render a scene using Blender
  User input objects rotation, translation, scale
  User input camera parameters
  User input trajectory
  Output imagery and metadata

## Slide 11: Blender Object Placement Validation
Object placement via scene.xml
Manual Inspection of vertices in Blender Application

## Slide 12: Blender Photogrammetric Validation
Developed a checkerboard “room” and moved cameras around the inside with 100 random translation, rotations
Used 5 different focal cameras
Extracted Corners in Matlab using Harris
Compared to expected projected based on camera
Half Pixel Bias

## Slide 13: Proof of Concept
Scene in Blender
Photoscan Pointcloud
Error Assessment
Render Images

## Slide 14
Add 3 meters flat water
Some structures half in water
Colored blue just for this figure
Blender Simulating Water Refraction

## Slide 15: Error Assessment after Photoscan Processing Using Known Camera Calibration (Fixed) vs Solving with SFM (Float)
caxis = [-0.2 0.2]
No Water
Intrinsic Float
Water
Intrinsic Fixed
Water
Intrinsic Float

## Slide 16: ToDo: Add Material Input in XML
How to generate cm scale resolution over 100m x 100m plane
  Option A: 10,000 x 10,000 image as texture
    Might crash Blender, not scaleable to km scale field site
  Option B: Tiling and Layering
    Tile the same textures repeatedly, and layer various textures
Currently the texture is set by the obj file
  This means for any texture, a new obj file must be made
Goal is to have a default texture for every object, but also a “textures” folder which the user can pick from

## Slide 17: ToDo: Validate Material Texture resolution/sharpness
Need to make sure that if the resolution of the imagery isn’t being downsampled or smoothed by the renderer
Seimens Target
Tribar array

## Slide 18: ToDo: DOCUMENTATION
Document focal length validation
Document principal point validation
Document Order of Rotations in Blender
  (Maybe want to use quaternions for this since Blender Euler is inconsistent)
Generate More OBJ files
Develop Image post-processing Script (vignetting, distortion, noise, blur)

## Slide 19: ToDo: Decide on Committee
Potential Committee Members? (in no particular order)
  GCR: Mike Bailey (Computer Graphics)
  Mike Olsen
  Craig Glennie
  Michael Starek
  Rob Fisher (ERDC-GRL doing SFM work)
  Craig Rodarmel

## Slide 20: Extra Stuff
Github repo: https://github.com/hokiespurs/BlenderPythonTest
  Need to get me to give you access so you can see issues, and code updates
Need a cool acronym
In Depth Details on XML format on next few slides

## Slide 21: Scene XML Format

## Slide 22: Object Library
*.txt
objectLibrary.txt
Indicates local xyz coordinates of “markers”
0,0,0 of object defines “control”

## Slide 23: Trajectory XML format

## Slide 24: Sensor XML format