## Slide 1: October Research Update

## Slide 2: V1.0 of Workflow
Automated Rendering
Formatted Output Files
Basic Object Database
No Lighting Enabled
  (shadeless)

## Slide 3: Input: Sensor.xml

## Slide 4: Input: Trajectory.xml

## Slide 5: Input: Scene.xml

## Slide 6: Input: Object/Texture Database
9 Primitive shapes
Various OBJ files with textures
  House
  Power Lines
  Car
  Hilly Topography
  Ideas?

## Slide 7: Output:
xyz of each control point (xyzControl.csv)
xyz of each fiducial point (xyzFiducial.csv)
xyz roll pitch yaw of each camera (Trajectory.csv)
Camera Intrinsic parameters (Sensor.xml)
Pixel coordinates of each marker in each image
Pixel coordinates of each fiducial in each image
Model folder with obj of the scene
Log folder with debugging info
Images folder with rendered imagery

## Slide 8: Image Postprocessing
Add Image Distortion
  k1,k2,k3,k4,p1,p2 Brown Coefficients
Vignetting
  ΔI = v1 + v2 * r + v3 * r^3 where v coefficients are normalized by maximum r
Salt and pepper noise
  Defined by a probability of each and random number function
Gaussian Noise
  Defined by a mean and variance
Gaussian Blur
  Defined by sigma
Raw Render
Postprocessed

## Slide 9: Two Example Scenes
“foo”
House + Noise + Water
63 Nadir Images (20MP)
“river”
House + Noise + Water
25 Nadir Images (20MP)

## Slide 10: Photoscan Quick Analysis
Error <1mm when given camera extrinsics, intrinsics, GCP positions, and sub-pixel Coordinates of GCPs

## Slide 11
Model of Scene

## Slide 12
Water Removed

## Slide 13
Faces of Model Exposed

## Slide 14
RGB Pointcloud Overlaid

## Slide 15
Model to Pointcloud Calculation
-10cm to 10cm

## Slide 16: Initial ‘foo’ observations
“submerged” points under the water cube are too high
GCPs experienced mixed pixel effect (dense reconstruction)
~+ 5cm noise on the flat surface… despite “sub mm” GCP accuracy
-5cm to 5cm
1m x 1m GCP

## Slide 17: Initial “river” Observations
Blue = water
-0.5m to 0.5m
-1.5m to 0m
1.5m too shallow
Possible to experiment with many variables and make depth correction equation?
depthcorrected = f(SFM calculated depth value, altitude, focal length)
water

## Slide 18: Paper Outline
Abstract
Intro, why relevant and novel
Background (put research in context)
Describe Computer Graphics to render a scene
  How, why beneficial?
How to Validate a Computer Generated Image
  Validate Object Placement (if automating placement)
  Validate rotation conventions
  Validate photogrammetric accuracy (fx,fy,cx,cy)
  Validate Texture resolution and “sharpness”
Description workflow/methodology I developed
Proof of Concept Experiment
  Hypothesis: “Do Independent GCPs bias accuracy of resultant pointcloud?”
  Experiment Design/Methodology
  Results
  Conclusion
Conclusion/Future Work/ Implications of Methodology

## Slide 19: TODO
Write!
Grow object and texture database
Develop Experiment to Test “independent GCP bias”
Write!
Make Figures
Write more