## Slide 1: Refraction Simulations
9/15/2017

## Slide 2: Processing Workflow
Workflow is mostly automated
XML schema used as input to both simUAS and agiproc
  Matlab is used to generate XML files due to familiarity
simUAS (Blender + Python + Matlab)
  Batch Process Simulations
  Output Simulated Imagery and Metadata
Agiproc (Photoscan + Python)
  Process all simulations in Photoscan
  Output Pointcloud and other Computed Parameters
Matlab
  Generate Simulation XML Files
user input
Matlab
  Generate Photoscan Processing XML Files
user input
Matlab
  Process and Analyze Data
  Generate Figures + Computed Equations
user input

## Slide 3: Goal: Simulate SfM Refraction Induced Error
Water IOR = 1.33
Perceived Location
True Location
Error

## Slide 4: Simple Experiment Introducing Refraction
Z = 0
Z = Altitude
Z = -depth
Water IOR = 1.33
hFOV
“Water Bucket Experiment”
Overlap %

## Slide 5: Overlap Percent Computed at Water Surface. Actual Overlap increases with depth
Z = 0
Z = Altitude
Z = -depth
Water IOR = 1.33
hFOV
“Water Bucket Experiment”
Overlap %
“actual” Overlap % ( not used)
Notes: “actual overlap increases with depth”

## Slide 6: Wider hFOV means camera positions must be more spread out to maintain overlap %
“Water Bucket Experiment”
Z = 0
Z = Altitude
Z = -depth
Water IOR = 1.33
Overlap %

## Slide 7: Texture on Seafloor is also scaled to ensure consistent texture between experiments
WaterBucketExperiment
Z = 0
Z = Altitude
Z = -depth
Water IOR = 1.33
Overlap %

## Slide 8: For this experiment with flat water, absolute altitude does not change results
=
*This will change if surface waves are added

## Slide 9: Fishtank Experiment Simulations
Buck Island Texture with Random RGB Noise
121 Images
  Flight Lines: 11 x 11
  2000 x 2000 pix
  No Nonlinear Distortion
  Perfect nadir and uniformly spaced EO
80% Overlap/Sidelap (at water surface)
100% Transparent water
No Specular Reflections
Notes: Replace this figure

## Slide 10: Pointcloud accuracy is broken into 3 regions
Region A:
All Data
Region B:
Clip with Flight Lines
Region C:
Clip by Full Viewing Geometry
Easting
Northing
Image FOV
Each Dot represents a camera position
This arrangement represents:
80% overlap
80% sidelap
Square Image

## Slide 11: Water Bucket Experiment Simulations (121)
Experiment Parameters
Altitude = 50m
Water Depth/Altitude = [0.01, 0.05, 0.10, … , 0.50] (11)
hFOV = [30,40,50,…,120] (10)
Agisoft Processing Parameters
Trajectory Input With No Uncertainty Added
Camera Position Accuracy = 0.01m
Camera IO set as Fixed
General Alignment = Medium
Optimization On
Dense Reconstruction = Medium, Filter = Aggressive

## Slide 12: Pointcloud For Each Simulation is Processed in Matlab (Region B Used)

## Slide 21: Further Exploration of this Experiment
Replicate plots for other bulk statistics (variance, median, etc)
Compute local variance (eg. Fuzz in the data)
Effect of Agisoft camera EO accuracy parameter
Differentiate Statistics for each “Region”
Easting
Northing

## Slide 22: Future Work
Equation for depth correction as a function of
  Altitude
  Depth
  Field of View
Test Equation Validity
  More advanced simulations with less “perfect” imagery
  Real world data

## Slide 23: Future Experiments?
Accuracy as a function of:
RTK Accuracy
Distribution of Above/Below Water GCPs
Wave Field (Period, Amplitude, Frequency Spectrum)
Non-Nadir Imagery
Variable Bathymetric Depths and Slopes
Overlap/Sidelap
Bottom Texture
IOR Accuracy
Camera Nonlinear Distortion