## Slide 1: Utilization of Simulated UAS Imagery to Assess the Accuracy of Structure from Motion Algorithms for Bathymetric Mapping
Structure from Motion and Multi-view Stereo algorithms have shown success in generating pointcloud data of bathymetry when imaged from unmanned aircraft systems (UAS) using various processing approaches. A basic approach to processing these data utilizes commercial structure from motion (SfM) software that does not account for refraction at the water surface. Errors introduced by this omission propagate into the resultant pointcloud, and measured water depths are predominantly too shallow. Methods ranging from submerged ground control targets to post-processing scale factors have been implemented to correct for these errors. Here, a simulated image rendering workflow (simUAS) is utilized to simulate different experiments that include water refraction and surface waves wherein images are generated along a simulated UAS flight path. These data are processed using commercial software and various processing methodologies, and the output pointclouds are compared to the control model data. The pointcloud error is quantified for various scenarios to determine the effect of camera, flight, and processing parameters on the accuracy of the resultant pointcloud. Lessons learned from the experiments are presented and compared to preliminary results from a real world field experiment.

## Slide 2: Utilization of Simulated UAS Imagery to Assess the Accuracy of Structure from Motion Algorithms for Bathymetric Mapping
Richie Slocum
Tim Battista
Brian Costa
Christopher Parrish
Wayne Wright

## Slide 3: Outline
Structure from Motion(SfM) Overview
Bathymetric Structure from Motion Challenges
Simulating UAS flights methodology
Simulation Results

## Slide 4: Structure from Motion
Image based 3D pointcloud generation
CPU intensive
With only images, the relative orientation between cameras is computed, but the coordinate system and scale are off
Adding Camera Pose estimates and/or GCPs puts the data into a real world coordinate system

## Slide 5: Structure from Motion
Minimize reprojection error
Output:
  Sparse pointcloud
  Camera pose estimates
  Camera calibration
Yilmaz, Ozgur & Karakus, Fatih. (2013)

## Slide 6: Dense Matching
Algorithm to generate a more dense pointcloud
Two of the most common are:
    MultiView Stereo(MVS)
    Semi-Global Matching(SGM)
*often this is included in “SfM software”

## Slide 7: Bathymetric Structure from Motion
Water IOR = 1.33
Perceived Location
True Location
Error
Refraction Induced Error

## Slide 8: Bathymetric Structure from Motion

## Slide 9: 3D Refraction Error

## Slide 10: simUAS
Image rendering methodology to simulate UAS imagery for SfM accuracy assessments
Full control of Independent Variables
simUAS (Blender + Python + Matlab)
  Batch Process Simulations
  Output Simulated Imagery and Metadata
Agiproc (Photoscan + Python)
  Process all simulations in Photoscan
  Output Pointcloud and other Computed Parameters
Matlab
  Generate Simulation XML Files
user input
Matlab
  Generate Photoscan Processing XML Files
user input
Matlab
  Process and Analyze Data
  Generate Figures + Computed Equations
user input

## Slide 11: Example Simulation
How does the “dense quality” in Agisoft Photoscan affect pointcloud accuracy?
Slocum and Parrish, 2017

## Slide 12: Example Simulation
77 Images
  A5000 Camera w/ ~72° hFOV
  5456 x 3632 pixels
75% Overlap/Sidelap
No added uncertainty
  10 GCPs
  Trajectory
  Camera Calibration

## Slide 13
1. Generate Model

## Slide 14
2. Texture Model

## Slide 15
3. Add Lighting to Scene

## Slide 16
4. Add Cameras

## Slide 17
5. Render Imagery

## Slide 18
6. Postprocess Imagery
Lens Distortion
Vignetting
Gaussian Noise
Salt/Pepper Noise
Gaussian Blur
ZOOM

## Slide 19
7. Process Data Using SfM

## Slide 20
8. Generate Sparse Pointcloud

## Slide 21
9. Generate Dense Pointcloud

## Slide 22
10. Compare Dense Pointcloud to Mesh

## Slide 23
11. Compute Cloud to Mesh Distances

## Slide 24
Qualitative Results

## Slide 25
Lower Photoscan Dense Quality = round corners
Qualitative Results

## Slide 26
Compute error by comparing to groundtruth data with no uncertainty
Quantitative Results

## Slide 27
As Dense quality increases
  Total points increase
  Accuracy improves
  Processing Time Increases
*CPU processing power can be a limiting factor
Quantitative Results

## Slide 28: Bathymetry Experiment
How is SfM accuracy affected by:
- Camera Field of View
Water Depth
Overlap/Sidelap

## Slide 29: Bathymetry Results

## Slide 30: Future Work
Compare simulations to real world data
Assess methods to correct refraction induced error
More realistic simulations
  Add water waves
  Add noise to UAS GPS
  Vary seafloor texture

## Slide 31: Conclusion
simUAS helps quantify SfM errors over a wide range of conditions
Topo Summary
  Denser the better,
Bathy summary
  Narrower FOV is better for bathy

## Slide 32: Questions